## Slide 1: T2K Near Detector Upgrades and Plans for T2HK
Thorsten Lux
On behalf of the
ND280 Upgrade Working Group

## Slide 2
Notes: Sk 4pi detector

## Slide 3
ND Purpose: Measurement of neutrinos before oscillation
ND components:
UA1 magnet: 0.2 T
0 detector (POD)
2 Fine Grain Detectors (FGD):
  target, FGD2 with H2O
  XY scintillator bars
  1 ton each
3 Time Projection Chambers (TPC)
Electromagnetical Calorimeter (ECAL)
Side Muon Range Detector (SMRD)

## Slide 4
T2K-II
aim: systematics from 5-6% to 4%
beam power upgrade: 485 kW  1.3 MW
statistics: 3E21 POT (2018)  20E21 POT (2026)
Aim for CPV observation in optimal scenario at 3σ
arXiv:1609.04111
Phys. Rev. D, 96:092006, 2017
arxiv:1609.04111
Notes: Updated table for 2018 presented in other talks

## Slide 5
SuperFGD
HA-TPC
HA -TPC
 beam

 | Current (FGDs) | Upgrade (FGDs + SuperFGD)
Target mass (tons) | 2.2 | ~4.2
TOF
N280 Upgrade replace POD by:
1 fine graned scintillator target (SuperFGD)
2 high angle TPCs (HA-TPC)
6 time of flight panels (TOF)
CERN-SPSC-P357
“4” detector

## Slide 6
SuperFGD
JINST 13 (2018) no.02, P02006
scintillator, WLS fibers + MPPCs
classical 2D approach reconstruction limitations
new 3D approach: 1x1x1 cm3 cubes with 3 WLS fibers
size: ~1.8x0.6x2 m3

## Slide 7
SuperFGD

e

p
Simulation studies:
high granularity allows excellent pattern recognition
light yield from the 3 fibers helps to distinguish 1 from 2 particles => e/ separation
significant improvement on p reconstruction efficiency

## Slide 8
SuperFGD
Cube production by injection mold method at INR RAS ( uncertainty ~35 m)
Reflector coating (~50 m) by chemical etching Uniplast (Russia)
2017: prototype of 5x5x5 tested at CERN testbeam:
  light yield
  cross talk
  timing resolution

## Slide 9
SuperFGD: Is it scaleable?
prototype of 9216 cubes
size: 8x24x48 cm3
1728 fibers/MPPCs
3 type of MPPCs
adapted Baby MIND electronics (based on CITIROC chip) for readout
Testbeam at CERN beginning of July
e, , , protons and  (!)

## Slide 10
SuperFGD:
Single track
Pion beam
Photon beam
Stopping proton
Simulation
Data
very successful data taking
important step towards full size detector
detailed data analysis ongoing
Notes: Photon momentum simulated between 0.2 and 0.6 GeV/c. Data not known, electron beam had 0.7 GeV/c.

## Slide 11
HA-TPC:
2 rectangular TPCs
inner dimensions:
  1.8 m wide
  0.7 m height
  2 x 1.06 m drift
single gas volume
composite material FC
radiation length: 2-3% X0
8 resistive MicroMegas
T2K gas: 93% Ar, 3% CF4, 2% iC4H10
Cathode voltage: ~25 kV
readout electronics based on AFTER chip
10% p/p at 1 GeV/c
Material | Thickss (mm)
Copper coated polymide film | ~ 0.15
Aramid Fiber Fabric (Kevlar) | 2.00
Aramide HoneyComb panel | 30.00
Aramid Fiber Fabric (Kevlar) | 2.00
Polymide film (insulation) | ~ 0.10
Strips (double later) on Kapton foil | ~ 0.15
TOTAL | ~34.40

## Slide 12
avalanche size in MM few microns => no charge sharing between pads
adding resistive layer to spread charge (NIM A518 (2004) 721) => reduction of electronics channels
first prototype tested with cosmics and 15 cm drift at Saclay
testbeam with 150 cm drift end of August
HA-TPC:
Insulator ~100 m
PCB
Resistive layer ~75 m
+ HV
Amplification gap ~100 m
e

## Slide 13
Baseline choice:
Cast plastic scintillator: EJ-200
8 SiPM (6x6 mm2) directly coupled to scintillator
readout from both sides
tested in CERN testbeam 2017
~70 ps time resolution for 1.5 m bars achieved
TOF:
JINST 12 (2017) no.11, P11023 (arXiv:1709.08972)

## Slide 14
TOF:
ND280 panels: 12x230x1 cm3
readout electronics based on MUSIC ASIC (UB) and SAMPIC digitizer (LAL)
purpose: identify if particles from target to magnet and improve backward efficienty for current tracker
Magnet
Magnet
or
or

## Slide 15
data
simulation

## Slide 16
Beyond T2K II:
T2K-II will improve systematics to 4%
aim for HK is 3%
idea is to add intermediate detector
Water Cherenkov detector doped with Gd
intense R&D program
2 phases:
  Phase 0: 50 ton test experiment at Fermilab or CERN (2021/22)
  Phase 1: full detector, movable (2025 and beyond)
HK talk on the 16th of August

## Slide 17: Conclusions
ND280 and Beam Upgrade for T2K-II
  High angle acceptance and low momentum measurement by SuperFGD, HA-TPCs and ToF counters
  R&D and simulation studies in progress
  Proposal submitted Jan 2018 (SPSC@CERN & PAC@J-PARC)
  Beam power increased to 1.3 MW
Schedule for the ND280 Upgrade:
  June - August 2018: SuperFGD and HA-TPC beam test @ CERN
  Acknowledgement: Many thanks to CENF for support!
  End of 2018: Technical Design Report
  2021: Installation and commissioning in Japan
  Reduction of systematics to about 4%
Plans for time beyond T2K-II well progressing:
  Intermediate water Cherenkov detector, movable
  Aim: reduce systematics to 3%

## Slide 18
BACKUP SLIDES

## Slide 20
Event displays (decay candidate)
150 ns
Muon life time is 2µs

## Slide 21
e/ Separation in ND280 Upgrade Target
  Goal to distinguish e/ events that are single-track, electron-like, low momentum (200 < p < 600 MeV/c)
  Distinction between 1 () and 2() MIP events using the MPPC light yield from the tracks
    Considering the light yield before and after the tracks split into different scintillator segments
z
y
Notes:     e-e+ pair where the positron was not reconstructed as a separate track due to the low momentum
    GEANT4 SuperFGD 2D particle gun track projection as a function of the total photo-electron (p.e.) counts

## Slide 22
A Photon beam in T9 area
Principle
e- beam
Cu radiator
MDX magnet
0.51 T.m
hodoscope
(measures electron momentum
 photon energy)
 beam
A. Blondel, L. Gatignon
may need a position detector
best is probably
around 2 GeV/c e-
for 200-800 MeV
photons
(should be simulated)