## Slide 1: STEREO
D. Lhuillier, CEA - Saclay

## Slide 2: ILL Site
ILL site, Grenoble - France:
57 MW, compact core < 1m
[8.9–11.1] m from core, possible extension to 12.3 m.
High level of reactor background
15 mwe overburden
No oscillation
First cell
Last cell
Goal: look for relative spectrum distortions in identical cells
6 target cells

## Slide 3: Strategy of the Stereo Measurement
Oscillation pattern based on relative shape in identical cells
  Take advantage of Gd-doped liquid scintillator technology to measure accurate spectra shape.
Cosmic rays induced background is the final limitation:
  Overburden from water channel
  Online rejection using PSD (stat)
  Subtraction of residual background using reactor OFF periods (syst)
Massive shielding against reactor induce accidentals (stat uncertainty)
Sensitive test of the sterile neutrino hypothesis
New reference measurement of pure 235U neutrino spectrum.

## Slide 4: Detector Design
Reflective plates to suppress dependence on vertex position
Double wall vessel
Central cells in acrylic, filled with Gd-doped LS (90 x 90 x 37.5 cm)
PMTs coupled to LS via a thick acrylic buffer for a better homogeneity
Outer crown (no Gd) to improve energy reconstruction and detection efficiency

## Slide 5: Detector Design
Detector vessel is built. Working on top lid machining and inner coating
The acrylic buffers will be delivered this week
Delivery of all remaining components expected on late February 2016
Assembly at CNRS-LPSC in Grenoble before transportation to ILL in April 2016.
Detector vessel
Acrylic buffers

## Slide 6: Liquid Scintillator
LAB 75% → protons target
PXE 20% + DIN 5% → light yield and PSD
Gd-complex 0.2% + 1 %THF → neutron capture
PPO + Bis-MSB → wavelength shifters
l ≳ 5 m
Stable
Transparent
proton recoilsc
electron recoils
PSD

## Slide 7: PMTs
8” PMT: New Hamamatsu R5912-100 with improved Quantum Efficiency, 30% at 420 nm
Tests are handled by MPIK Heidelberg in their Faraday lab
New PMTs basis with decoupling system delivered by LPSC-Grenoble
All components tested and to be delivered this month.

## Slide 8: Detector Response
400 pe/MeV expected
Resolution 11.5% (RMS for 2 MeV positrons)
Neutron efficiency 60% with a delayed signal above 5 MeV
Outer crown:
  Reduces the difference on neutrons efficiency between center and border cells to 4%
  Keep the response to prompt signals identical in central and border cells

## Slide 9: Detector Response
Linearity of the PMTs and electronics validated in the physics range of interest.
The quenching of low energy recoiling electrons introduces a dependence on the way the total energy of an event is deposited.
Circulation of radioactive sources inside and around the detector.
Monitoring of the detector response by a set a LEDs.

## Slide 10: Calibration
3 light injection points per detector cell
+ 12 in the outer crown
Circulation of radioactive sources in calibration tubes

## Slide 11: Calibration
Extra information from the deployment of sources underneath and around the detector vessel. Outer crown can be used to veto Compton events
Possibility to tag the direction of a 511 keV g-ray using a 22Na source coupled with a small LYSO crystal
Setup under test with a mockup of the detector vessel.

## Slide 12: Prototype Cell
The response of a prototype cell has been tested this year.
Same height and width than final config, ½ length.
Equipped with acrylic buffer and reflective plates
Light signals induced in the whole volume by:
  Source outside the vessel
  Movable light diffuser
  Source in central calibration tube

## Slide 13: Prototype Cell
Heigth (cm)
Detected charge (a.u.)
60Co in central tube
Top
Center
Small vertex dependence (~5%):
  Validates the reflective plates
  Negligible impact on energy resolution
Good agreement with the simulation

## Slide 14: Electronics
Dedicated electronics hosted in TCA crate
Front-end boards are already tested and validated
  8-channel FADC 14 bits 250 MHz sampling
  Qtot, Qtail, tCFD and pulse
  Gain x1 and x20 for single PE
  First level programmable trigger (FPGA) validated with muon veto
Trigger board: second level programmable trigger (FPGA) taking into account the 3 detectors : Target cells, outer crown, veto
LED driver for light calibration
All cards already delivered and tested
TCA crate
Trigger board
Front-end

## Slide 15: Data Acquisition
Configuration and data collection done using standard ILL software NOMAD
Development of low level driver done at LPSC fully operational
Slow-control, monitoring, alarm system under development

## Slide 16: Internal Shielding
65 T of lead against external g-rays
6 T Polyethylene against fast neutrons
B4C layers against thermal neutrons
Soft Iron + m Metal layers to shield stray B-field
Muon Veto
Internal shieldings
Magnetic shieldings
Overview
Seismic study finalized, Fire study still in progress
Muon veto umbrella to tag cosmic ray induced background

## Slide 17: Muon Veto
Water-Cerenkov detector
  4x2.6x0.25 m3 water + wavelength shifter (4MU)
  20 PMTs on the top
  Tyvek diffuser
Results from prototype
  Excellent overall efficiency 98.5% and stable
  PMTs mapping to reduce sensitivity to g-rays
Final detector fabricated and soon delivered

## Slide 18: Site Characterization
Stereo
Extensive g, m and n measurements on site performed in 2014-15:
Ge, NaI,3He and fast-n detectors inside various shielding
Data analysis coupled simulation of the detector setups
MCNPX simulations of the reactor and main neutron lines
Energy spectrum and location of all sources
Design of shielding to meet the specifications of <100 Hz in prompt window and 1 Hz in delayed window.
Modular PE shielding
Directionality studies
Deconvoluted g-spectrum
Complete reactor simulations

## Slide 19: Shielding Configuration
Old “H7” line removed
Combination of heavy concrete, lead and B4 barriers to block g and n fluxes.
STEREO

## Slide 20: Shielding Configuration
Neutron absorbers added in neighbor primary casemate
STEREO

## Slide 21: Shielding Configuration
Last front wall installed in Sept. 2015
10 cm lead + 10 cm PE
STEREO

## Slide 22: Shielding Configuration
Final reinforcement of the side wall foreseen this winter.
STEREO

## Slide 23: Sensitivity
400 n per day during 300 days
Signal/Background = 1.5
Detection and reconstruction effects from GEANT4 simulation
Neutrino flux uncertainties + 4% norm uncertainty
Visible Ee+ > 2 MeV
En > 5 MeV  edet=60%
dEscale = 2%

## Slide 24: New Reference 235U Spectrum
120 000 n expected
Highly enriched fuel
 pure 235U fission spectrum
Daya Bay Aug. 2015
RENO Nov. 2015
Caution: RENO normalization?
Measurement complementary to Double Chooz, Daya Bay and Reno near detectors.
Could bring new insight into the deviation at 5 MeV (see Julia’s talk)

## Slide 25: 5 MeV Bump
Evolution of the sensitivity when introducing the 5 MeV Bump as a new uncertainty in the predicted spectrum (50% of the amplitude).
To first order the oscillation phase is not compatible with an isolated deviation around 5 MeV.

## Slide 26: Conclusion
Sensitivity contours cover the Reactor Anomaly. Emphasis on control of the detector response to control shape distortions.
Final design validated by prototypes and seismic studies
Several external shielding walls have already been installed
Most parts of detector are under fabrication or already delivered, the schedule is now driven by the delivery of some shielding parts and the final safety agreement.
The detector integration will take place at LPSC-Grenoble in Feb-March 2016
First data expected in summer 2016