## Slide 1: Status of consideration of implementation of nuSTORM at CERN
Mike Lamont
12th August 2018
Jonathan Gall, John Osborne – SMB
Ken Long – Imperial University, London
Marco Calviani –EN/STI and team
Claudia Ahdida – HSE/RP and Radiation Protection (RP) team
Wolfgang Bartmann - TE/ABT

## Slide 2: PBC - scientific goal
Explore the opportunities offered by the CERN accelerator complex to address some of today’s outstanding questions in particle physics
These experiments would typically:
  enrich and diversify the CERN scientific program,
  exploit the unique opportunities offered by CERN’s accelerator complex and scientific infrastructure,
  complement the laboratory’s collider programme (LHC, HL-LHC and possible future colliders).
  Examples of physics objectives include searches for rare processes and very-weakly interacting particles, measurements of electric dipole moments, etc.

## Slide 4: nuSTORM@FNAL proposal
Neutrinos from STORed Muons - Proposal to the Fermilab PAC – July 2013
Fast extraction from MI at ~120 GeV
  8e12 protons/1.33 s cycle
Conventional pion production and capture (horn)
  Quadrupole pion-transport channel to decay ring
Low-energy muon decay ring

## Slide 5: FNAL proposal
Fermilab report details:
  Decay ring support building
  Target hall support building
  Near detector service building
  Far detector
  Cryogenic building
Fermilab design – Surface buildings site plan
Well developed, and costed, proposal – a reference point together with input from Ken, Jaroslaw and team

## Slide 6: CENF - short baseline neutrino facility
Primary beam
~600 m from target area
Secondary beam
In front of EHN1
Near Detector Facility
@456 m from target,
EHN1 extension
Far Detector Facility
@1600 m from target
North Area
100 GeV/c
Fast extraction
Protons per cycle 4.8e13
 4.5x1019 pot/yr
15 m deep

## Slide 7: Summary of CENF studies
Lots of work done and executed
Advanced integration of beam elements, plus ventilation and radiation protection
Civil engineering works also performed
… then stopped in 2014
Lots of input for new projects, such as BDF (and/or nuSTORM)

## Slide 8: SPS
Rav = 1.1 km
LSS2: slow-extraction
LSS3: RF
LSS6: fast extraction
LSS4: fast extraction
TI2: LHC
Beam 1
TI8: LHC
Beam 2
AD
LEIR
2
ELENA
ISOLDE
LSS1: injection,
internal beam dump
AWAKE
(formerly CNGS)
LINAC3
LHC
BEAM
DIRECTION
HIRADMAT
LINAC4
nTOF
[1] J.B. Adams, The CERN 400 GeV Proton Synchrotron, 1977
North Area (NA): max 450 GeV
SHiP

## Slide 9: nuSTORM @ CERN - parameters
Preliminary parameter table developed for discussion
Now aiming at 6 GeV muons instead of 3.8 GeV -> scaled version of ring

## Slide 10: nuSTORM@CERN
SPS can deliver the beam
  e.g. CNGS 400 GeV/c fast extraction
  CNGS approved to 22.5e19 POT
    i.e. 5 years at 4.5e19 POT/year
  From 2008 to 2012 delivered 81% of approved total
In co-existence/competition from other users:
LHC, North Area (+HiRadMat, AWAKE) at present
Growing list for future (SHiP, KLEVER…)

## Slide 11
2 - slow
6 - fast
4 - fast
North Area
ex-CNGS
AWAKE
LHC
LHC
HiRadMat

## Slide 12: nuSTORM@CERN - siting options
North Area:
  Kick @ LSS1; extract @ LSS2
  Transport to North Area:
    Issues:
      Congestion, radio-protection, slow extraction
CERN to Gran Sasso beam line:
  Beamline directed “down hill” in molasse to serve Gran Sasso
  Would put nuSTORM ring deeper than necessary
  Existing target area hot
LSS6:
  Served West Area Neutrino Facility
  HiRadMat now operational
Preferred option “semi-greenfield” …

## Slide 13
Extraction septa
LSS6
SPS
LHC
LHC B1
nuSTORM
HiRadMat

## Slide 14: Extraction from TT61
Possible reach for: 1.8 T (Magenta) or 1.6 T (Yellow) bending fields

## Slide 15: nuSTORM@CERN – SPS Extraction
Extraction from LSS6
  100 GeV protons, large emittance beams (FT beams in SPS)
  May need some changes to beam line equipment in this area – to be confirmed at later stage
TT61 transfer
  Appeared the best location for junction cavern and transfer to new line
Civil Engineering to look at feasibility in detail based on parameters
  Minimum single plane bending radius – 300 m
  Minimum bending radius for horizontal and vertical bending – 480 m
Initial siting guidance from accelerator beam transfer group

## Slide 16: Civil Engineering - development
Latest options 4 and 5
Option 4 with far detector in Prevessin
Option 5 with minimised tunnel length
CERN land
Within molasse
TT61 Extract – junction cavern
Typical section at 2-2
Typical section at 1-1
Plan view showing options 4 and 5
Potential far detector at Prevessin
Route de l’Europe
Option 4
Option 5
CERN Meyrin

## Slide 17: Civil Engineering – Option 4
Muon ring scaled to 6 GeV
far detector in Prevessin

## Slide 18: Civil Engineering – Option 5

## Slide 19: Civil Engineering – Option 4 & 5
1
1
2
2
3
3
TN(Neutrino)
TI2
TT10
TT61

## Slide 20: Civil Engineering - Site Access
Existing access roads to point 1 SPS, SM18 and Bat. 846
Overhead electrical supplies
Woodland
1
2
2
1

## Slide 21: Likely construction method - molasse
Standard tunnelling techniques to be used in competent molasse.
Reduced disruption at surface particularly roads and services

## Slide 22: Target complex development - CENF
Marco Calviani

## Slide 23: Target complex development - CENF
Marco Calviani

## Slide 24: Antiproton production target (AD-T)
Why: it might be an interesting alternative to nuSTORM-like design
Fixed target in the PS complex to produce antiprotons for the AD physics
  26 GeV/c, 1.5*1013 ppp
  450 ns (4 bunches)
  0.5x1 mm2
  Iridium target, water-cooled
  Magnetic horn, 400 kA
  Collimators, dump, quadrupoles, dipoles (dog-leg)
Marco Calviani

## Slide 25
Marco Calviani

## Slide 26: nuSTORM proposal
FNAL proposition based on a NuMI (AP0) style target station design, i.e. equipment in a “chase”
arXiv:1308.6822v1
Marco Calviani

## Slide 27: Production target
FNAL proposes a 2l target based on NuMI design (graphite, water-cooled)
  Is this the most optimized solution for a 5 GeV/c pion beam??
  Inconel-based was proposed but not analysed
Can we use the experience out of the Ir-based or Ta-based segmented target from AD-T?
  Certainly a more point-like source for the focusing horn?
Ta and Au were also considered in the proposal
Marco Calviani

## Slide 28: Magnetic horns
nuSTORM proposed NuMI-style horns
CERN experience with CNGS ones
LAGUNA-LBNO studies allowed developing a genetic algorithm for shape optimisation (still employed today by LBNF)
Recently AD magnetic horn rebuilt from scratch (calculations & production & soon pulsing tests)
Link for AD-horn R&D
Marco Calviani

## Slide 29: Injection line and proton absorber
Injection line has a single dipole  significant radiation in the decay ring !!!??
Proton absorber similar to a TIDVG-like assembly? Not studied in the FNAL study (?)
arXiv:1308.6822v1

## Slide 30
Proton dump
  O(100 kW)  TIDVG4-5 design (modified as external dump) appropriate (no worries here)
Pion dump
  O(2-3kW [ref])  passive (iron) absorber should be enough
Is the pion dump required if we have a dog-leg?
1
2
arXiv:1308.6822v1
3.7 GeV/c arcs
5 GeV/c injection

## Slide 31: Ideas for nuSTORM
A target area based on AD-T concept with vertical handling (a-la-CENF/NuMI) might be possible alternative
  Target area much smaller and dose rate confined
~Site independent… could be even at a depth
Marco Calviani

## Slide 32: Preliminary draft target complex development
Muon decay ring
Decay ring support building
Primary Beam absorber
Target complex
Based initially on FNAL designs, developed for CERN situation
Initial ideas:
  Production target, focusing horn, pair of capture quadrupole, collimators ++ dipoles (not in FNAL proposal)
  Helium Vessel
  Underground cavern with shaft to surface building offset
Further work required to understand requirements in detail. Currently quite preliminary.
Near detector

## Slide 33: Detector Hall
Currently based on FNAL proposals ≈50 x 16.5m in plan.
Near detector foreseen
Possibility for far detector to be considered.

## Slide 34: Radiation Protection
Well established methodology at CERN for radiation protection studies
Detailed evaluation was performed for CENF
Resources not available for a detailed study at present but RP are in the loop
Based on CENF and wide ranging experience and the fact the proposed nuSTORM installation is in the molasse and at a depth of >20 m - looks OK
Target at ~15 m

## Slide 35: Conclusions 1/2
SPS can provide beam and fast extraction
Potential extraction point and site identified
Initial civil engineering sketches performed
Initial thoughts on target/horn/absorbers (considerable expertise at CERN)
Target complex concept sketched
Radiation protection – no dedicated study yet performed but at first sight, given proposed depth, should be manageable

## Slide 36: Conclusions 2/2
NB: really only a sketch at the moment – limited resources
“Exploratory study” to go to ESPP update in December
  10 page “executive summary” plus a more detailed CERN report