## Slide 1
CHANDLER: A Technology for Surface-level Reactor Neutrino Detection
Jonathan Link
Center for Neutrino Physics, Virginia Tech
WIN2023 AT SYSU ZHUHAI CAMPUS, CHINA
July 3 - July 8, 2023

## Slide 2
The MiniCHANDLER Prototype, open during assembly to show the cubes and 6Li-doped ZnS sheets
The CHANDLER* Reactor Neutrino Detector
CHANDLER was designed, from the start, to be a robust, mobile detector technology, suitable for a wide range of applications.
It uses a highly-segmented array of plastic scintillating cubes as the neutrino target and positron detector,
And thin sheets of lithium-6 doped zinc sulfide (ZnS) scintillator to tag the neutron capture.
*Carbon Hydrogen Anti-Neutrino Detector with a Lithium Enhanced Raghavan optical lattice

## Slide 3: Neutron Identification in CHANDLER
The positron signal is formed in the cubes and gives short duration light pulse of about 10 ns,
Neutron capture light comes from the ZnS, which releases its scintillation light over much longer time scale (~200 ns)..
For each hit cell, we can compute a simple neutron ID variable as the ratio of the pulse integral to the pulse height.
Higher neutron ID means more neutron-like.
pulse integral
pulse height

## Slide 4: Neutron Identification in MicroCHANDLER
The x and y neutron IDs show a clear neutron/positron separation
When the source is removed the events in the neutron region mostly go away.
The neutrons candidates that remain are consistent with the cosmic ray flux.

## Slide 5
The MiniCHANDLER Prototype, open during assembly to show the cubes and 6Li-doped ZnS sheets
Light is transported along the rows and columns of cubes by total internal reflection, and readout by photomultiplier tubes.
The CHANDLER* Reactor Neutrino Detector
CHANDLER was designed, from the start, to be a robust, mobile detector technology, suitable for a wide range of applications.
It uses a highly-segmented array of plastic scintillating cubes as the neutrino target and positron detector,
And thin sheets of lithium-6 doped zinc sulfide (ZnS) scintillator to tag the neutron capture.
*Carbon Hydrogen Anti-Neutrino Detector with a Lithium Enhanced Raghavan optical lattice

## Slide 6
Light from the sheets is absorbed in the cubes and retransmitted by a wavelength-shifter so that it can also be captured by total-internal-reflection.
The Raghavan Optical Lattice allows us to achieve excellent energy and spatial resolution over a large, unbroken detector mass.
The cubes are optically connected in layers, and sandwiched between sheets of 6Li-loaded ZnS scintillator for neutron detection.
Light from the cubes is transported by total-internal-reflection, along the rows and columns of cubes, to the edge of the detector, where it is readout by photomultiplier tubes.
The Raghavan Optical Lattice
Jonathan Link

## Slide 7
The MiniCHANDLER Prototype, open during assembly to show the cubes and 6Li-doped ZnS sheets
Light is transported along the rows and columns of cubes by total internal reflection, and readout by photomultiplier tubes.
We use this high segmentation to tag the gammas from positron annihilation, and thus reject correlated backgrounds like fast neutrons.
The CHANDLER* Reactor Neutrino Detector
CHANDLER was designed, from the start, to be a robust, mobile detector technology, suitable for a wide range of applications.
It uses a highly-segmented array of plastic scintillating cubes as the neutrino target and positron detector,
And thin sheets of lithium-6 doped zinc sulfide (ZnS) scintillator to tag the neutron capture.
*Carbon Hydrogen Anti-Neutrino Detector with a Lithium Enhanced Raghavan optical lattice

## Slide 8
200 ns
200 ns
e+
p
n
3H
4He
6Li
n
p
n
3H
4He
6Li
Cosmic-Ray Fast Neutron
γ
γ
Detected Light
time
Positron (e+)
Annihilation γs
Neutron Capture
10 ns
50 μs
time
Detected Light
Proton
Neutron Capture
10 ns
50 μs
High segmentation allows us to tag the positron annihilation gammas interacting in neighboring cubes.
Neutrons are tagged by the slow scintillation decay time of the zinc sulfide scintillator (200 ns vs 10 ns).
The time ordered coincidence of the positron and the neutron tag separates IBDs from background.
In the field we saw 85 correlated fast neutrons for every IBD event, so we need powerful tools to reject them!
Inverse Beta Decay (IBD)
The Signal and the Noise

## Slide 9
MiniCHANDLER in Pictures
The 80 kg, 80 channel MiniCHANDLER detector was completed in fall 2016.
It was commissioned and installed in our Mobile Neutrino Lab…

## Slide 10: The Mobile Neutrino Lab
The MiniCHANDLER prototype was installed in our Mobile Neutrino Lab and deployed to the North Anna Nuclear Generating Station.

## Slide 11
The Mobile Neutrino Lab at North Anna
Jonathan Link

## Slide 12: The Mobile Neutrino Lab
The MiniCHANDLER prototype was installed in our Mobile Neutrino Lab and deployed to the North Anna Nuclear Generating Station.
MiniCHANDLER would become:
  The first demonstrated mobile neutrino detector,
  The first unshielded reactor neutrino detector, and
  One of the world’s smallest neutrino detectors.

## Slide 13
The MiniCHANDLER Analysis
Phys. Rev. Applied 13, 034028 (2020)

## Slide 14: The IBD Event Selection
The inverse beta decay candidates include all positron-like events in the 1000 μs preceding a neutron.
The positron candidate energy is reconstructed from the pattern of PMT light collected in each detector plane.
We apply a spatial separation cut between the positron and neutron.
Topological selections are used to reject multiple proton recoils and tag evidence of the annihilation gammas:
  Total energy outside the primary cube <1 MeV
  No single cube outside the primary cube with E>511 keV
  At least one cube outside the primary with energy >100 keV

## Slide 15: Fitting Δt for Correlated Events
We then sorted our IBD candidates into energy bins of 1 MeV.
In each bin, the positron-neutron Δt distribution was fitted with an exponential plus flat distribution,
This is how we extracted the time-correlated event rate as a function of the positron candidate energy.
Phys. Rev. Applied 13, 034028 (2020)
Random Coincident Events
Correlated Events

## Slide 16: Time Correlated Fast Neutrons
The fast neutron rate is inversely correlated with atmospheric pressure.
Most of the time correlated events are fast neutrons,
and their rate is independent of the reactor power.
After a pressure correction, we found that the average correlated rate in the reactor-off period was lower than in reactor-on by about 4 events/hour.
No topological selections applied.
Random events with Δt < 500 μs
Reactor-off
Which is consistent with the expected inverse beta decay rate.
Phys. Rev. Applied 13, 034028 (2020)

## Slide 17: The IBD Analysis Results
To further eliminate the correlated background, we performed a reactor-off subtraction.
We used energy bins beyond the signal region (from 8 to 20 MeV) to scale the reactor-off absolute rate to match the reactor-on rate.
We fit this excess to the inverse beta decay spectrum from Monte Carlo (black histogram).
Phys. Rev. Applied 13, 034028 (2020)
The excess below 8 MeV are neutrino events.

## Slide 18: Topological Selection
The topological selections were essential to extracting a significant signal in MiniCHANDLER:
These selections will improve dramatically with the improved optics.
And, a larger detector will better contain the annihilation gammas and multiple proton recoils.
Signal Significance [Δχ2]

## Slide 19
CHANDLER Future Prospects

## Slide 20: Future Upgrades
Going from MiniCHANDLER to full CHANDLER, there are several known enhancements:
New optics: improves energy resolution, pattern recognition and background rejection.

## Slide 21
511 keV
Compton Edge
1273 keV Compton Edge
511 keV
Compton Edge
1273 keV Compton Edge
(As used in the original MiniCHANDLER)
We rebuilt our MicroCHANDLER prototype with half new optics.
We used a 22Na source to compare the energy response in the new and old optics.
The new light collection improves the energy resolution by at least a factor of 2.
The annihilation gamma Compton edge and continuum are now distinct features.
MiniCHANDLER Upgrades: New Optics

## Slide 22: Future Upgrades
Going from MiniCHANDLER to full CHANDLER, there are several known enhancements:
New optics: improves energy resolution, pattern recognition and background rejection.
Larger detector: faster event accumulation and better detection efficiency from neutron and annihilation gamma containment.
PMTs on four sides: improves the pattern recognition and the energy resolution.
Half cubes: increases 6Li tagging efficiency and lowers the random coincident background rate.

## Slide 23: Half Cubes
The half cubes upgrade doubles the effective 6Li density in the detector.
The opposing PMTs are offset by a half-cube to take advantage of the extra spatial information.
Configuration | 6Li Capture
Full Cubes | 51%
Half Cubes | 69%
The half cubes upgrade increases the 6Li capture efficiency by 35%, but it only increases the cost of the detector by only 12%.
Half cubes lowers the capture time and capture spatial separation, which reduces the random coincident background rate.
Time to 90% Capture
229 μs
120 μs
Volume for 90% Capture
37 cubes
24.5 cubes

## Slide 24: Future Upgrades
Going from MiniCHANDLER to full CHANDLER, there are several known enhancements:
New optics: improves energy resolution, pattern recognition and background rejection.
Larger detector: faster event accumulation and better detection efficiency from neutron and annihilation gamma containment.
PMTs on four sides: improves the pattern recognition and the energy resolution.
Half cubes: increases 6Li tagging efficiency and lowers the random coincident background rate.
Electronics upgrade: lowers cost, improves data quality and pattern recognition.

## Slide 25: Electronics Upgrade
PMT High Voltage Power Supply
Data Acquisition Electronics
Old Electronics
We are pursuing a major upgrade to our electronics.
This base puts the high voltage, ADC and a fully programmable trigger, all at the PMT.
  Uses power over Ethernet
  No channel-to-channel crosstalk
  No signal attenuation
  ADC dynamic range goes from 12 bits to 14 bits
  Dynamic trigger threshold for superimposed hits
  On-board, programmable neutron/positron ID
All-in-one PMT Base
New Electronics

## Slide 26: Final Thoughts
We’re upgrading MiniCHANDLER for a redeployment at North Anna this spring.
This upgrade includes new PMTs and light guides, a new voltage-divider base, and one plane of half cubes.
Unfortunately, we will not have the all-in-one base for this deployment; a consequence of the global semiconductor crisis.
This deployment will test improved topological selection criteria based on better energy resolution.
CHANDLER is one of two technologies selected for the Mobile Antineutrino Demonstrator project, a collaboration with Livermore National Lab.
We are approved to build a 650 kg CANDLER detector in 2024.